## Slide 1: Intro to Coding
Session 2: Potentiometers + Servos

## Slide 2: Doorbell

## Slide 3: Embedded Systems = Hardware + Software
Hardware: Physical Devices
Shields
Push Buttons
Potentiometers (again)
Buzzers (piezoelectric)
Software: Digital Tools
Define & Variables
Serial Monitor Pt 2
Conditional Statements

## Slide 4: Shields
Attach onto an Arduino
Provide specific functionality

## Slide 5: Buzzers
Produce sound
Change Pitch

## Slide 6: New Code!

## Slide 7: #Define
Similar to variable creation
Cannot change during your code
Saves space/memory on board

## Slide 8: Making Sounds
tone(pin, frequency)
tone(pin, frequency, duration)

## Slide 9: Serial Print
Serial.print - Prints to Monitor
Serial.println -Prints to Monitor & goes to a new line

## Slide 10: Commenting out
Add comments to a line //
Temporarily makes board skip that code

## Slide 11: Code Play
Comment out noTone and second delay command
What could I change about the code to make the frequency twice as high?

## Slide 12: Buttons
Two states (pushed or not pushed)

## Slide 13: New Code!

## Slide 14: Conditional Programming
Conditions allow board to ‘make choices’
If button pressed
Turn on Light
Else (button is not pressed)
Turn off Light

## Slide 15: Multiple Conditions
If button1 and button2 pressed
Get an orange
Else IF button1 pressed
Get an apple
Else IF button2 pressed
Get a grape
Else
No Fruit

## Slide 16: Order Matters
If button1 pressed
Get an apple
Else IF button2 pressed
Get a grape
Else IF button1 and button2 pressed
Get an orange
Else
No Fruit

## Slide 17: Arduino Example
if (button_state == true) {
digitalWrite(LED, HIGH);
}
else {
digitalWrite(LED, LOW);
}

## Slide 18: Challenge - Doorbell
Create a new code that acts as a doorbell
  When button is pressed, LED lights up and a sound is created
  When button is not pressed, LED is off and sound stops